Build Process
- Compiler
- Pre-processing stage
  - Main.c --> Main.i
  - Code generation
    - C language statements will be converted into processor architecture level mnemonics
    - Main.i -->Main.S
- Assembler Stage
  - Main.S --> Main.o (Relocatable Object file)
- Linking stage
  - All the object files will be taken by linker and resolves the symbols Merge all the data from similar sections of multiple object files and generates an executable file(*.o --> executable) which is .elf formats.

---
sections
.data
  - Read-Write portion of program which stores global and static initialized variables
.text
  - A read-only section containing the actual instructions of the program.
.bss
  - Stores global and static uninitialized variables
.rodata
  - Read only data

---
crt /Startup file
- initialize global pointer,stack pointer
- set up trap vector
- check for initialization routine and call it if one exists
- Can also contain vector table
- zero the bss segment
- disable and clear interrupts
- check for floating point architecture and enabling FS bits in riscv isa
- After copying segments (data,itim,ram,LIM) at this stage we can execute c code