RISC-V

---
TABLE OF CONTENTS
- What is RISC-V
- RISCV-ISA
  - Previlege ISA
  - Unprivileged ISA
- RISC-V Registers
- Calling Convention
- Hart
- Instruction Types
- Interrupts
- Sifive Hifive1 board
  - Boot Process
- Toolchain
- Build Process
  - Compiler,assembler,linker
- Different data and sections of program
- Debugging

---
RISCV-ISA
- RISC-V ISA is an open source implementation of a reduced instruction set computing(RISC) based instruction set architecture(ISA) driven through open collaboration, enabling freedom of design across all industries and domains.
- What is ISA
  - An instruction set architecture (ISA) is an abstract model of a computer. It is also referred to as architecture or computer architecture. A realization of an ISA, such as a central processing unit (CPU), is called an implementation. Some ISAs you may have heard of include x86, ARM, MIPS, PowerPC, or SPARC. All of these ISAs require a license to implement them. On the other hand, the RISC-V ISA is provided under open source licenses that do not require fees to use
- RISC-V was begun with a goal to make a practical ISA that was open-sourced, usable academically, and deployable in any hardware or software design without royalties.
- The RISC-V authors are academics who have substantial experience in computer design, and the RISC-V ISA is a direct development from a series of academic computer-design projects, especially Berkeley RISC. RISC-V was originated in part to aid all such projects
                  https://en.wikipedia.org/wiki/RISC-V

---
What is not Risc-V
- As an Instruction Set Architecture, RISC-V itself is not “open source” in the same way that software is open, as an ISA is not made of source code. It is, however, an open specification, and it is released under a Creative Commons license
- Not open source hardware as Linux is for operating systems

---
RISC-V ISA
- Risc-v ISA is broken in two parts
  - Unprivileged Specification
  - Privileged Specification
- Privileged Specification
  - As its name suggests, the privileged specification contains descriptions of the RISC-V ISA which operate in Machine Mode (M-mode) or Supervisor Mode (S-mode).
  - RISC-V currently has three privilege levels: User Mode (U-mode), Supervisor Mode (S-mode), and Machine Mode (M-mode). U-mode is for user processes, S-mode is for kernel and/or device drivers, and M-mode is used for bootloader and/or firmware. Each privilege level has access to specific Control and Status Registers (CSRs), and higher privilege levels can access the CSRs of those less privileged levels
  - This specification also contains additional functionality required for running rich operating systems like Linux.
- Unprivileged Specification
  - Simply put, the unprivileged specification details items that are not related to machine mode (M-mode) or to Supervisor Mode (S-mode). The unprivileged specification includes the base ISA as well as extensions to that base like integer (I), float (F), double (D), compressed instructions (C), and many more

---
Unprivileged specification
- The base instruction sets describe the instruction format, basic integer instructions, load and store instructions, and other fundamental details of the ISA. We break these up into several bases:
- RV32I - Integer 32 bit
  - contains 47 unique instructions.
- RV32E - Reduced RV32I for embedded purposes
- RV64I - Integer 64 bit
- RV128I - Integer 128 bit
- All these “Base ISA’s” either reduce or extend off the RV32I base instruction set. As an example, RV64I widens the integer registers and the supported user address space to 64 bits.
      https://riscv.org/risc-v-learn-online/

---
Privileged Modes(M)
- Machine Mode
- M-mode is used for low-level access to a hardware platform and is the first mode entered at reset, when the processor finishes initializing and is ready to execute code
- M-mode can also be used to implement features that are too difficult or expensive to implement in hardware directly.
  - A good example of this would be a watchdog timer implemented in low level software (firmware) which helps the system recover from faults.

---
RISC-V REGISTERS
- The RV32I base integer ISA includes 32 registers, named x0 to x31. The program counter PC is separate from these registers, in contrast to other processors such as the ARM-32.
- The first register, x0, has a special function: Reading it always returns 0 and writes to it are ignored. As we will see later, this allows various tricks and simplifications.
- CSR (Control and Status Registers) for each Modes
https://github.com/riscv-non-isa/riscv-asm-manual/blob/master/riscv-asm.md

---
RISC-V REGISTERS

---
RISC-V calling Convention
https://riscv.org/wp-content/uploads/2015/01/riscv-calling.pdf

---
Hart
A hardware execution context, which contains all the state mandated by the RISC-V ISA: a PC and some registers. This terminology is designed to disambiguate software's view of execution contexts from any particular microarchitectural implementation strategy.

---
INSTRUCTION TYPES
- Register-to-Register
  - Arithmetic and Logical operations
- Control Instructions alter the sequential control flow
- Memory Instructions move data to and from memory
- CSR Instructions move data between CSRs and GPRs; the instructions often perform read-modify-write operations on CSRs
- Privileged Instructions are needed by the operating systems, and most cannot be executed by user programs

---
Instructions
- Arithmetic
- Logical
- Load/Store
- Branch
  - Conditional
  - Unconditional
- Set Instructions(flag instructions)
- System instructions

---
Arithmetic Instructions

---
Logical

---
Load/Store

---
Branch

---
Integer Computational Instructions

---
System Instructions

---
commands
riscv64-unknown-elf-as -o -march=rv32imac rv-hello.o hello-world.S
riscv64-unknown-elf-ld -o rv-hello rv-hello.o
OR
riscv64-unknown-elf-gcc -o rv-hello helloworld.S -nostdlib -static

---
Software
- Spike ??
  - Proxy kernel
- Riscv32 toolchain
- Freedom studio

---
Build Process

---
Sifive Hifive-1 board

---
sections
.data
  - Stores global and static initialized variables
.text
  - Stores code
.bss
  - Stores global and static uninitialized variables
.rodata
  - Read only data

---
Toolchain
- Compiler
  - Pre-processing stage
    - Main.c --> Main.i -->Main.S
- Assembler
  - Main.S --> Main.o
- Linker
  - Deifining memory regions
  - Merging all the data from similar sections of multiple object files.
  - Generates an executable file(*.o --> executable)

---
- Startup file
  - initialize global pointer,stack pointer
  - set up trap vector
  - check for initialization routine and call it if one exists
  - Can also contain vector table
  - enter c runtime start up file
- C runtime file
  - zero the bss segment
  - disable and clear interrupts
  - check for floating point architecture and enabling FS bits in riscv isa
  - After copying segments (data,itim,ram,LIM) at this stage we can execute c code